## Slide 1
CS533 · Machine Learning for EDA
Power-Aware Recipe Synthesis
ML-Guided Simulated Annealing for Automated Logic Synthesis Optimization
Daksh Agarwal (230101123) · Aditya Shukla (230101115)
Kartik Maheshwari (230101116) · Girish M. Bhajantri (230101040)

## Slide 2
Problem Statement
01
Combinatorial Explosion
Synthesis recipe space grows exponentially with sequence length. Exhaustive search over 20-command recipes from even 4 commands yields 4²⁰ ≈ 10¹² combinations — far beyond compute budget.
02
Evaluation Bottleneck
Each candidate recipe requires a full ABC synthesis + OpenROAD place-and-route flow for accurate post-layout power measurement — too expensive for inner-loop search.
Goal:
Given an unoptimized AIG, find a sequence of synthesis commands that minimizes post-layout power within a practical time budget.

## Slide 3
System Architecture
Input AIG
Circuit Design
▶
Feature
Extraction
9-dim structural vector
▶
ML Power
Predictor
Neural surrogate scorer
▶
SA Search
Loop
80-step annealing
▶
Validation
Real synthesis run
⟳ SA Search Loop — ML predictor scores recipes without running synthesis; only best candidate gets full ABC validation
Stage A — Train Power Predictor
25 benchmark designs × 16 recipes
Full OpenROAD post-layout power as ground truth
9 structural AIG features + recipe embedding as inputs
Train/val/test split by design ID
Stage B — SA Recipe Search
Start with random 20-command recipe
Mutate: replace (50%) or swap (50%)
Score via ML predictor
Accept/reject via Metropolis criterion
Validate top candidate with real ABC + OpenROAD

## Slide 4
Dataset Generation & Feature Engineering
25
Benchmark Designs
16
Synthesis Recipes
~300
Labeled Instances
9-dim
Feature Vector
1
Feature Extraction
2
Logic Synthesis
Compute 9-dim structural AIG vector (nodes, edges, PIs/POs, latches, AND nodes, depth, fan-in/out)
3
Ground-Truth Power
Full OpenROAD flow: placement → routing → static power analysis → post-layout value
4
Data Aggregation
Features + recipe ID + power → training dataset.
Apply recipe to AIG → tech-mapped netlist via Berkeley ABC

## Slide 5
Power Predictor — Neural Architecture
AIG Features (9-dim)
↓
MLP Layer · ReLU · Dropout
↓
MLP Layer · ReLU · Dropout
↓
⊕ Concatenate
↓
Dense (144) · ReLU · Dropout
↓
Predicted Power
Recipe ID
Embedding (16-dim)
Hyperparameters
hidden_dim:
128
recipe_emb_dim:
16
dropout:
0.2
optimizer:
Adam lr=0.001
Training Details
Split by design ID
Loss: MSE | Target transform: log1p option
Z-score normalization on all 9 AIG features

## Slide 6
Simulated Annealing — Recipe Search
1
Initialize
Random 20-command recipe from AIG-safe pool
2
Mutate
50% replace random cmd · 50% swap two positions
3
Score
ML predictor
4
Accept/Reject
Always accept if lower. Otherwise P = exp(−ΔE/T)
5
Cool
Exponential temperature decay over 80 steps
AIG-Safe Command Pool
balance (b)
rewrite (rw)
refactor (rf)
resub (rs)
Restricted to avoid AIG state corruption from commands like choice/fraig
Acceptance Criterion
Always accept if E_new ≤ E_current
Otherwise: P(accept) = exp( −ΔE / T )
Steps
80
Recipe Length
20 commands
Seed
42
Temp Schedule
Exponential

## Slide 7
Power Predictor — Performance
MAE — Test
3.11 mW
Few-Shot Learning (LODO Cross-Validation)
Leave-One-Design-Out: model trained on N-1 designs, tested on held-out design.
Samples (k) | Improvement
k = 1 | 9%
k = 3 | 13%
k = 5 | 27%
Chart: Few-Shot Improvement vs Samples
| k=1 | k=3 | k=5
Improvement (%) | 9 | 13 | 27

## Slide 8
SA Search — Convergence & Behaviour
Chart: SA Convergence — fpu_orig (Predicted Power)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80
Predicted Power Proxy | 25 | 23.4 | 22.1 | 21 | 20.2 | 19.5 | 19 | 18.5 | 17.8 | 17.5 | 17 | 16.8 | 16.5 | 16.3 | 16.2 | 16.1 | 16
Key Observations
Rapid improvement in early iterations (high-T exploration phase)
Convergence plateau after ~50 steps — search locks onto local minimum
SA explores non-intuitive command orderings that manual scripts miss
80 steps sufficient for strong relative gains; more steps may help further

## Slide 9
Results — SA vs. Best ABC Baseline (3 Validation Designs)
Chart: Post-Layout Power (mW)
| max_orig | ethernet_orig | fpu_orig
Best Baseline | 2.83 | 69.11 | 20.42
SA Recipe | 2.29 | 51.14 | 16.24
Design | Best Baseline | SA Power | Reduction
max_orig | 2.83 mW (syn2) | 2.29 mW | 19.3%
ethernet_orig | 69.11 mW (syn3) | 51.14 mW | 26.1%
fpu_orig | 20.42 mW (syn2) | 16.24 mW | 20.5%
26.1%
ethernet_orig
Largest single-design gain
19.3%
max_orig
Smallest (still beats all 3)
20.5%
fpu_orig
Consistent improvement

## Slide 10
Chart: 
Extended Results — 8 Benchmark Designs
Chart: 
| ac97_ctrl | aes_orig | aes_secworks | aes_xcrypt | des3_area | ethernet | fpu_orig | max_orig
Best Baseline | 11577.09 | 19242.5 | 21912.39 | 20862.09 | 3623.34 | 69110.52 | 20420.54 | 2831.7
SA Recipe | 9608.03 | 16355.75 | 17529.64 | 22322.34 | 3333.16 | 51141.78 | 16244.14 | 2286.13
7/8
Designs Beat Baselines
14.75%
Average Improvement
18.36%
Median Improvement

## Slide 11
Improvement (%) vs. Best Baseline — All 8 Designs
Chart: 
| ac97_ctrl | aes_orig | aes_secworks | aes_xcrypt | des3_area | ethernet | fpu_orig | max_orig
Improvement (%) | 17.46 | 15.35 | 19.94 | -7 | 8.04 | 26.13 | 20.45 | 19.27

## Slide 12
Validation Methodology
Fair, Consistent Comparison: Both SA-generated recipes AND all 3 ABC baselines are validated through the identical OpenROAD post-layout flow for power measurement.
1
SA Generates Best Recipe
Top candidate from 80-step SA run (20 commands)
2
ABC Synthesis
Apply recipe to initial AIG → optimized technology-independent Verilog netlist
3
OpenROAD Place & Route
Full physical design: placement → CTS → routing using standard cell library
4
Static Power Analysis
Post-layout power analysis — same flow for SA and baselines (syn, syn2, syn3)
5
Compare Results
SA power vs. best of {syn, syn2, syn3} — all measured identically

## Slide 13
Discussion & Limitations
Why it works
ML predictor identifies power-sensitive directions without expensive synthesis in the inner loop
SA explores non-intuitive command orderings missed by human-engineered scripts
Limitations
Only 8 designs evaluated; broader statistical coverage on 25 benchmarks still needed
SA runs only 80 steps; larger budgets may uncover further improvements

## Slide 14
Future Work
01
Sequence-Aware Encoding
Replace Hamming with RNN / LSTM / Transformer to encode full command sequence, enabling the predictor to learn syntactic and semantic patterns.
02
Multi-Objective (PPA)
Extend cost function to jointly optimize Power, Performance (depth), and Area (nodes). Use Pareto-front SA to expose the full trade-off surface.
03
Broader Benchmarks
Run SA on all 25 benchmark designs and increase steps. Statistical analysis over larger design family will give stronger generalization evidence.
04
Transfer Learning
Meta-learning or domain adaptation to allow the predictor to quickly adapt to entirely new circuit families with minimal fine-tuning examples.

## Slide 15
Thank You
for your patience
CS533 · Machine Learning for EDA · Power-Aware Recipe Synthesis